## Slide 1: N12 Data-in criteria
Process | Clock Uncertainty | Timing Derate | Period Discount | Wire Load Model | Synthesis Corner
N12 | PLL/DLL jitter | 0 | 50% for the DFT , P & R effects , POCV, V/T OCV , aging | ZWLM | ssgnp m40c (WCGC)
Process | Clock Uncertainty | Timing Derate | Period Discount | Wire Load Model | Synthesis Corner
N12 | PLL/DLL jitter +5ps | Net derate (side file) Spatial derate (side file) 3% for memory and IO cell (without POCV) 5% for level shifter 5% for Macro cell (without POCV) | 3% for the DFT 5% for backend implementation 8% for POCV , V/T OCV Total 16% | - | ssgnp m40c (WCGC)
Synthesis (zero wire load)
Physical aware synthesis (POCV timing)

## Slide 2: N12 timing Sign-off Summary
N12
Timing Check | Library corner | RC corner | Process OCV | Local Voltage/Temperature | Spatial | Wire | Uncertainty | SI
Setup | ssgnp/0.9VDD/m40c ssgnp/0.9VDD/0c ssgnp/0.9VDD/125c | Cworst_Ccworst_T Rcworst_Ccworst_T | LVFM @ delay 3σ LVFM @ Constraint 3σ | (1a) Worst corner Voltage De-rating Lookup @ Capture Cell (1b) Worst corner Temperature De-rating Lookup @ Capture Cell | Spatial POCV side file @ Cell Delay | Wire POCV side file @ Wire Delay | PLL jitter + 5ps (DPT) | YES
Hold | ssgnp/0.9VDD/m40c ssgnp/0.9VDD/0c ssgnp/0.9VDD/125c | Cworst_Ccworst Rcworst_Ccworst | LVFM @ delay 3σ LVFM @ Constraint 3σ | (1a) Worst corner Voltage De-rating Lookup @ Launch and Data Cell (1b) Worst corner Temperature De-rating Lookup @ Launch and Data Cell | Spatial POCV side file @ Cell Delay | Wire POCV side file @ Wire Delay | 3ps (DPT) | YES
 | ffgnp/1.1VDD/m40c ffgnp/1.1VDD/0c ffgnp/1.1VDD/125c | Cworst_Ccworst Rcworst_Ccworst Cbest_Ccbest Rcbest_Ccbest |  | (2a) Best corner Voltage De-rating Lookup @ Capture Cell (2b) Best corner Temperature De-rating Lookup @ Capture Cell |  |  |  | 
(1a) Worst corner Voltage De-rating Lookup |  |  |  |  | (2a) Best corner Voltage De-rating Lookup |  |  | 
Nominal Voltage | RVT | LVT | ULVT |  | Nominal Voltage | RVT | LVT | ULVT
0.8 | 4.38% | 2.60% | 1.92% |  | 0.8 | 2.02% | 1.42% | 1.06%
(1b) Worst corner Temperature De-rating Lookup |  |  |  |  | (2b) Best corner Temperature De-rating Lookup |  |  | 
Nominal Voltage | RVT | LVT | ULVT |  | Nominal Voltage | RVT | LVT | ULVT
0.8 | 0.70% | 0.20% | 0.40% |  | 0.8 | 0.60% | 0.70% | 0.80%

## Slide 3
Confidential information
  The material is being disclosed to you pursuant to a non-disclosure agreement between you or your employer and Faraday. Information disclosed in this presentation may be used only as permitted under such an agreement.
Legal notice
  The information contained in this presentation is intended to provide a general guide as to which product is suited for a given requirement and shows suggested product applications. Specified functions and properties for products are only valid when handling instructions and other stated conditions and recommendations have been considered and followed. All descriptions, illustrations and dimensions in the information represent general particulars and do not form part of any contract. All information is provided “as is”, with no guarantee of completeness, accuracy, timeliness or of the results obtained from the use of the information, and without warranty of any kind, express or implied, including but not limited to warranties of performance. All information is subject to change without prior notice. Faraday assumes no responsibility whatsoever for any errors or inaccuracies about the information.