## Slide 1: 2022 Major Release Design Kit Update fetm, ftcv
DD/LDF/Ollie
Version MR202201

## Slide 2: 2022 fetm major release

## Slide 3: Fetm update
UPF flow
  generate ETM by upf
Litmus
  To replace CCD in ftcv checking constraint rule
  Litmus can be only applied on the os7 machine
Env
  source ~cadman/env/FTC.env
  source ~cadman/env/fetm.env

## Slide 4: Extract model original flow vs upf flow
Primetime Extract model
Add related_power_pin
Add fa_related_power
Add internal_power
Add leakage_power
Library Compiler generate db
Gen upf and no_pg netlist
Primetime Extract model with upf
Add leakage_power
Design Compiler generate pglib
Add pad information
Add pad information
Library Compiler generate pgdb
Primetime Extract model
Add pad information
Add leakage_power
if $GEN_NO_PG_ETM
Step 5
Step 6.5
Step 4.5
Step 5
original flow
upf flow
Step 5

## Slide 5
step 1
check control file
step 2
Run genrp to generate *fapower
step 3
Check database
step 4
step 5
step 6
Use *fapower to generate pgmap
Modify SDC by removing boundary constraints
Run Primetime to generate ETM lib file
Move ETM libs and other necessary files to output folder
step 6.5
step 7
Generate pglib and pgdb from ETM libs (dc_shell, lc_shell)
Check ETM lib’s timing arc (CCD)
Generate db file (lc_shell)
step 1
check control file
step 2
Run genrp to generate *fapower
step 3
Check database
step 4
step 5
step 6
Use *fapower to generate pgmap
Modify sdc adjusting rule
Run Primetime to generate ETM lib with pg information by ETM upf flow
Move ETM libs and other necessary files to output folder
step 6.5
step 7
Modified
Check ETM lib’s timing arc (by Litmus, CCD, NO)
step 4.5
Generate upf file and no_pg netlist
Fetm will skip step 6.5 if ETM upf flow

## Slide 6: fetm I/O chart (GEN_ETM_BY_UPF flow)
Fetm
Sign off/ Dream System
PG Netlist
(*.v)
Timing Constraint
(*.sdc)
RC files
(*.spef)
pgmap
(*.pamap)
fetm control file
Pad pin list file
Powervalue list
(if 28nm)
AOCV_TABLE
Core , IO , Macro, IP Library
(*.lib *.db)
ETM lib
(*.pglib.gz, *.lib.gz)
Arc report
(.arcrpt, noarcpins.lis)
Log
(fetm.log)
optional
necessary

## Slide 7: fetm input / output
Fetm
Sign off/ Dream System
Netlist
(*.v)
Timing Constraint
(*.sdc)
RC files
(*.spef)
pgmap
(*.pamap)
fetm control file
Pad pin list file
(if 28nm)
AOCV_TABLE
Core , IO , Macro, IP Library
(*.lib *.db)
ETM lib
(*.pgdb, *.db
*.pglib.gz, *.lib.gz)
Arc report
(.arcrpt, noarcpins.lis)
Log
(fetm.log)
optional
necessary
powervalue list

## Slide 8: Fetm control file
genctrl (default | other options)
  GEN_ETM_BY_UPF = NO | YES generate ETM.pglib
  GEN_NO_PG_ETM = NO | YES generate ETM.lib
  MODEL_VALIDATION = NO | YES
  CHECK_ETM = CCD | LITMUS | NO
Fetm will go original flow if the options is all unset or set to default
Fetm will check the os version if CHECK_ETM is set to LITMUS

## Slide 9: Output files & New options in control file
Fetm
GEN_ETM_BY_UPF
Original flow
lib.gz db
pglib.gz pgdb
UPF flow
GEN_NO_PG_ETM
pglib.gz
lib.gz
NO
YES
YES
MODEL_VALIDATION
gba.out pba.out
YES
Model validation
NO
CHECK_ETM
arc.rpt
etm_check.rpt
CCD/LITMUS
Check ETM
NO
Fetm ends
Gen no_pg ETM
NO
orinigal flow

## Slide 10: Output ETM file
Original flow
  ETM.lib.gz、ETM.db PGLIB/ETM.pglib.gz、PGLIB/ETM.pgdb
UPF flow
  GEN_ETM_BY_UPF = YES GEN_ETM_BY_UPF = YES
  GEN_NO_PG_ETM = NO GEN_NO_PG_ETM = YES
  ETM.pglib.gz ETM.lib.gz、ETM.pglib.gz

## Slide 11: Step 4 - modify sdc adjusting rule
Original
  set_operating_conditions
  set_input_transition
  set_input_delay
  set_output_delay
  set_clock_uncertainty
  set_max_transition
  set_load
  set_drive
  set_driving_cell
  set_timing_derate
  set_propagated_clock
  remove_propagated_clock
Modified
  set_max_delay

## Slide 12: Step 4.5 - add genupf
Add new option “GEN_ETM_BY_UPF = { YES | NO }”, default is NO
Input file
  powervalue.list
  ${design}.pgmap
  ${design}.v
Output file
  ${design}_{ss|tt|ff}.upf
  ${design}.v.nopg
Fetm gets power & ground information from powervalue.list and pgmap for generating upf file with ETM upf flow.
Fetm parses netlist and pgmap to generate no pg netlist for ETM upf flow

## Slide 13: Step 4.5 - add genupf
powervalue.list is necessary for GEN_ETM_BY_UPF flow
fetm returns error if POWERFILE is missing
powervalue.list
  user have to fill in power ground information according to the pgmap
Turn on the POWERFILE option, and fill in the POWERFILE name in fetm.control

## Slide 14: Step 5 - add model validation
Fetm goes model_validation flow if MODEL_VALIDATION is set to YES
  MODEL_VALIDATION = { NO | YES }
Model validation flow generates two timing report of design and ETM wrapper, and compares the two timing reports to check the performance of ETM.
Model validation related file will be put in the directory, “.fetm_tmpdirxxx/model_validation/”
  design.tim timing report of design
  model.tim timing report of ETM wrapper
  *.gba.out compare_interface_timing of design.tim and model.tim
  *.pba.out compare_interface_timing of design.tim and model.tim after pba
Model validation can’t be applied in DMSA mode (VNC)
The command added into primetime script for model validation
  set_app_var hier_modeling_version 2.0
  extract_model -validate timing …

## Slide 15: Step 5 - modify primetime setting, fixed 2022/07/25
Original
  set extract_model_include_mcp_in_arc_value false
Modified
  set extract_model_include_mcp_in_arc_value false
mcp true mcp false
  0.430887 - (-0.819113) = 1.25
  0.426938 - (-0.823062) = 1.25

## Slide 16: Step 5 - modify primetime setting
Add (for gen_etm_by_upf flow)
  set enable_golden_upf true
  set extract_model_include_upf_data true
  set extract_model_upf_supply_precedence internal
Add (for model validation flow)
  set hier_modeling_version 2.0
  set model_validation_output_file *.pba.out
  set model_validation_save_session false

## Slide 17: Step 5 - modify
Fetm will return error while not applying “read_aocvm” command with the option “timing_aocvm_enable_analysis” is set to true during aocv flow
  set timing_aocvm_enable_analysis true|false
Remove addmargin in Step 5
  The user-defined margin added into ETM is no longer allowed.
Fix pad_cell attribute in ETM
  pad_cell will no longer being added twice

## Slide 18: Step 5 - modify
Add the ss*m40c_cmin corner for 40 nm in fetm_signoff_criteria
  file:///U:\DesignKitUsage\fetm\fetm_sign_off_corner.pptx
Fix the missing setup_ ss*m40c_cmin corner for 40 nm
  before
  After

## Slide 19: Step 6.5 - modify
Fetm will generate ETM.pglib and ETM.pgdb at step 6.5 with dc_shell and lc_shell in original flow.
Fetm will skip step 6.5 in ETM upf flow if the option “GEN_ETM_BY_UPF” is set to “YES”

## Slide 20: Step 7 - modify
Add a new option in control file “CHECK_ETM = {NO|CCD|LITMUS}”, default is CCD
“CHECK_ETM = NO”
  For pre stage, the ETM boundary constraint may be too complex to be checked
  Fetm will skip checking constraint rule
“CHECK_ETM = CCD“
  Fetm will check the constraint rule with CCD (original flow)
“CHECK_ETM = LITMUS”
  Fetm will check the constraint rule with Litmus
  Litmus can be only applied on the os7 machine

## Slide 21: Comparison of ETM upf flow and original flow
1

## Slide 22: Comparison of ETM upf flow and original flow
1
2
2

## Slide 23: Comparison of ETM upf flow and original flow
3
3

## Slide 24: Model validation usage

## Slide 25: Model validation usage
Fire primetime with design and ETM wrapper
Step 1: Modify pt script ( .fetm_tmpdirxxx/c*gen*.pt )
  set model_validation_save_session true (fetm default setting is false)
  #quit (remark “quit” at the end of pt script)
Step 2: Fire primetime and build design
  % pt_shell -f ${primetimeScript}
Step 3: Fire primetime and build ETM wrapper
  % pt_shell
  pt_shell> restore_session model_validation/model_validation.session

## Slide 26: Model validation usage
report_timing -rise_from txck25m_b_mux -rise_to po_rxd[0] -delay_type max -significant_digits 3
report_timing -rise_from txck25m_b_mux -fall_to po_rxd[0] -delay_type max -significant_digits 3
Ref: slack from design
Cmp: slack from ETM wrapper
Diff: $Ref - $Cmp

## Slide 27: Model validation usage
ETM wrapper
Design

## Slide 28: 2022 ftcv major release

## Slide 29: Ftcv update
Litmus
  To replace CCD in ftcv checking constraint rule
  Current rule reference checking by CCD are not all supported by Litmus
  U:\DesignKitUsage\ftcv\CCD_LITMUS_rule_reference.pptx
  U:\DesignKitUsage\ftcv\litmus_rulereference_22.10.pdf
Litmus flow
  source ~cadman/env/FTC.env
  source ~cadman/env/ftcv.env
  ftcv val $proj pre litmus
Output file
  litmus/*
  .ftcv_litmus.log

## Slide 30: Ftcv checking reports
litmus/*
  allLint.rpt
    check all constraint lint
  allRule.rpt
    check all constraint rule
  Boundary.rpt
    check io delay
  CLKuncertainty.rpt
    check clock uncertainty
  Clock.rpt
    check clock related constraint
  Conflict.rpt
    check sdc design

## Slide 31: Ftcv checking reports
litmus/*
  Explicit.rpt
    check exceptions
  FalsePath.rpt
    check false paths
  UnConstraint.rpt
    check CLK_DEF1
    Unconstrained clock: A clock pin does not belong to any clock tree (missing create_clock or create_generated_clock command)

## Slide 32
Confidential information
  The material is being disclosed to you pursuant to a non-disclosure agreement between you or your employer and Faraday. Information disclosed in this presentation may be used only as permitted under such an agreement.
Legal notice
  The information contained in this presentation is intended to provide a general guide as to which product is suited for a given requirement and shows suggested product applications. Specified functions and properties for products are only valid when handling instructions and other stated conditions and recommendations have been considered and followed. All descriptions, illustrations and dimensions in the information represent general particulars and do not form part of any contract. All information is provided “as is”, with no guarantee of completeness, accuracy, timeliness or of the results obtained from the use of the information, and without warranty of any kind, express or implied, including but not limited to warranties of performance. All information is subject to change without prior notice. Faraday assumes no responsibility whatsoever for any errors or inaccuracies about the information.