## Slide 1: genpglib.tcl
LDF/Ollie

## Slide 2: Script usage
Description
  genpglib.tcl
  A script for generating pgmap, pglib and pgdb
Flow chart
genpglib.tcl
pgmap
pglib
pgdb
control file
non-pg lib
-genpglib
(design cmpiler)
-genpgdb
(library compiler)
-genpgmap

## Slide 3: Script usage
Syntax
  -control $control_file_name
  -top $top_name
  -genpgmap
  -genpglib
  -genpgdb
Example
  # gen pgmap
  genpglib.tcl -top ${top_name} -control ${control_file_name} \
  -genpgmap
  # gen pglib & pgdb
  genpglib.tcl -top ${top_name} -control ${control_file_name} \
  -genpglib -genpgdb

## Slide 4: Script usage
Input
  linked or copied library ETM/*lib
  netlist
Output
  pgmap ${TOP}_${corner}.pgmap
  design compiler script ETM/script/*.gpglib.dc
  library compiler script ETM/script/*.gpgdb.lc
  pglib ETM/*.pglib

## Slide 5: Script usage
Input
Output

## Slide 6: Script usage
Flow steps
  Prepare a control file
  Create a directory named ETM and link or copy all the .lib into it
  Run script with the following command
  source ~cadman/env/FTCDEV.env
  source ~cadman/env/fetm.env
  genpglib.tcl -top ${top_name} -control ${control_file_name} -genpgmap -genpglib
  4. The .pglib will be generated by script and put in the directory ETM

## Slide 7: Control file template
The red information above is used for script parsing netlist and checking the connection of each port
The blue information above is used for script declaring the power/ground definition in pglib.
The red information above can be found in fetm control file
NETLIST = ${NETLIST_FILE} TOP = ${TOP_NAME} [CORNER_BEGIN] CORE_LIB = ${CORE_LIB_FILE} IO_LIB = ${IO_LIB_FILE} MACRO_LIB = ${MACRO_LIB_FILE} SPEF = ${SPEF_FILE} # CORNERMODE = [CORNER_END] #VOLTAGE_MAP_BEGIN # voltage_name ssa nn ffa VCC 1.10 1.00 0.90 GND 0.00 0.00 0.00 #VOLTAGE_MAP_END

## Slide 8: Control file example
example
NETLIST = FXLPDDR4CMSCFC100NSHI3L.v TOP = FXLPDDR4CMSCFC100NSHI3L [CORNER_BEGIN] CORE_LIB = IO_LIB = MACRO_LIB = /auto/s_FinFET/14LPP/libman/common/std_cell/arm/ARM_14LPP_HardIP_sc9mcpp84_base_rvt_c14/new/lib/ARM_14LPP_HardIP_sc9mcpp84_14lpp_base_rvt_c14_ssa_sigcmax_max_0p72v_m40c.lib /auto/s_FinFET/14LPP/libman/common/std_cell/arm/ARM_14LPP_HardIP_sc9mcpp84_base_lvt_c14/new/lib/ARM_14LPP_HardIP_sc9mcpp84_14lpp_base_lvt_c14_ssa_sigcmax_max_0p72v_m40c.lib /auto/s_ipd_proj/LPDDR/FXLPDDR4CCFC100HI3L/workspace/sridhar/0.1.0/FXLPDDR4CCFC100HI3L/others/release_to_APR/analog_phy/lib/pg/FXLPDDR4CCFC100NSHI3L_ssa_sigcmax_0p72v_m40c.pglib SPEF = FXLPDDR4CMSCFC100NSHI3L.spef.SigCmaxDP_ErPlus_m40c.gz CORNERMODE = [CORNER_END] #VOLTAGE_MAP_BEGIN # voltage_name ssa nn ffa GND 0.00 0.00 0.00 GNDA 0.00 0.00 0.00 GNDIO_DDR 0.00 0.00 0.00 VCC08K 0.72 0.80 0.88 VCC18A_REG 1.62 1.80 1.98 VCCIO_DDR 0.99 1.10 1.21 VDD 0.72 0.80 0.88 VSS 0.00 0.00 0.00 #VOLTAGE_MAP_END