## Slide 1: Merging Extracted Models
LDF / Ollie

## Slide 2: Contents
Introduction
Merged ETM Example
Merged ETM usage
Script Usage
Merging Model Issue
Reference
Appendix

## Slide 3: Introduction
Merging model overview
  Users can use the merge_models command to merge multiple single-mode ETM .lib files into a single multiple-mode ETM .lib file. The resulting merged ETM can then be set to its available modes by using the set_mode command in the PrimeTime tool.
  The models being merged must be consistent, with the same I/O pins, operating conditions (process/voltage/temperature), and so on.

## Slide 4: Introduction
Merging multiple modes into a mode group
  To create a merged model that merges multiple modes into a single mode group
  The resulting merged.lib contains mode-specific arcs where the model behaviors differ
merge_models \ -group_name {etm_mode} -mode_names {capture shift} -lib_files {capture.lib shift.lib} -output merged.lib -format {lib db}
library(“...”) { ... mode_definition (etm_mode) { mode_value (capture) {} mode_value (shift) {} } ... pin(“...”) { timing() { mode (etm_mode, “capture”); ... } timing() { mode (etm_mode, “shift”); ... } } }
Use the -mode_names option to specify the list of mode names.
Use the -lib_files option to specify the input .lib model files, exactly in the same number and order given in the -mode_names option.

## Slide 5: Introduction
Why do we need merged ETM?
  To reduce the amount of single mode ETM files
  single mode ETM * 3 merged ETM * 1
set link_path “* core.lib \\ IP_capture.lib” read_verilog TOP.v link_design TOP source TOP_capture.sdc
set link_path “* core.lib \\ IP_shift.lib” read_verilog TOP.v link_design TOP source TOP_shift.sdc
set link_path “* core.lib \\ IP_func.lib” read_verilog TOP.v link_design TOP source TOP_func.sdc
set link_path “* core.lib \\ IP_merged.lib” read_verilog TOP.v link_design TOP
source TOP_capture.sdc set_mode capture
source TOP_shift.sdc set_mode shift
source TOP_func.sdc set_mode func

## Slide 6: Merged ETM Example
Out-sourcing Merged ETM provided by Synopsys
  /home/oip/wrk/tmp/bowen_chen/OIP/SNPS/dwc_12g_phy_umc28hpcp_x4ns_8m1a1u_fc/lib_pg

## Slide 7: Merged ETM Example
mode_definition and timing arcs in merged ETM
  16bits & 8bits
  capture, shift and func

## Slide 8: Merged ETM Usage
How to specify the operating mode?
  set_mode ${MODE} ${CELL}
  set_mode 8bits u_CORE/u_USBHS/u_OTGPHY/u_FZOTG268HF0F
  The mode should be specified by “set_mode” in SDC
How to check if the mode is specified correctly?
  report_mode

## Slide 9: Merged ETM Usage
How does PrimeTime switch operating mode if there is no set_mode in SDC?
  The operating modes are both ENABLED if there is no set_mode in SDC

## Slide 10: Merged ETM Usage
fstaH checks if there are multiple enabled mode in SDC, and prints a ReportMode.rpt

## Slide 11: Merged ETM Usage
Another commands to check if the mode is specified correctly
  report_disable_timing
  With “set_mode 8bits”, the report_disable_timing returns that the timing arcs of 16bits are disabled by the mode
“Flag: m” indicates that the timing arc is disabled by “set_mode”

## Slide 12: Merged ETM Usage
Does Primetime accept “set_mode” if there is no merged ETM loaded?
  Primetime returns WARNING: UITE-132
Summary
  User should apply set_mode to get the desired mode timing from merged ETM
16bits Enabled
8bits Enabled
read_lib ${merged_ETM}
set_mode 8bits ${CELL}
16bits disabled
8bits Enabled
Primetime picks the worst timing for STA
Primetime picks the ENABLED timing for STA

## Slide 13: Script Usage
Script
  /home/eda/FTC_CADTOOL/EXE/merge_model.tcl
Syntax
  merge_model.tcl
    [-top ${TOP}] Specify the TOP name of single mode ETM
    [-runpt] If this option is specified, script runs primetime
    [-gendb] If this option is specified, script generate merged ETM by format of {lib db}
    [-val] If this option is specified, script validates merged ETM (extra input required)
    [-vnc] If this option is specified, script goes primetime dmsa flow with VNC
Example
  merge_model.tcl -top ${top_name}
  merge_model.tcl -top ${top_name} -runpt
  merge_model.tcl -top ${top_name} -runpt -gendb
  merge_model.tcl -top ${top_name} -runpt -gendb -val

## Slide 14: Script Usage
Note
  source primetime.env if the argument ‘-runpt’ is specified.
  Validation flow is optional since that there is no merged table in merged ETM, so the validating report will be all PASS
  Refer to appendix 1.* for the detailed information of validating flow
When to use
  For IP, the merging models steps will be completed by IPT check-in flow
  For partition blocks, the merging steps should be complete by users with merge_model.tcl

## Slide 15: Script Usage
(pre|post)_(lib|pglib) can be put into the directory and will be classified by script automatically
  single mode ETM collected and classified by script

## Slide 16: Flow chart
flow chart
Step 1
Search ETM files in the current directory
find stage
(pre/post)
find corner mode & PVT_RC
find etm format
(.lib, .pglib, …)
find mode (mode = file_name - top - stage - cornermode - pvt_rc - format)
Step 2
Check corner consistency between single mode ETM files
Step 3
Write merging ETM PrimeTime script
Step 4
Launch PrimeTime for merging ETM
Step 5
Check and rename the merged ETM
Step 6
Validate merged ETM
** NOTE **
The mode names in merged ETM are determined by single mode ETM filename
-top
-runpt
-val

## Slide 17: Input & Output
Input
  single mode ETM
Command
  /home/eda/FTC_CADTOOL/EXE/merge_model.tcl -top lds_cpu -runpt
Output
  merging_${stage}_${etmFormat}.pt merging ETM Primetime script
  merged_${stage}_${etmFormat} merged ETM directory (-runpt)

## Slide 18: VNC Primetime DMSA flow
Command
  -vnc
  -vnc_group ${GROUP_NAME}
  -vnc_multiproc ${MULTIPROC_NUM}
  -vnc_multicore ${MULTICORE_NUM}
Example
  merge_model.tcl -top ${top_name} -runpt -vnc
  merge_model.tcl -top ${top_name} -runpt -vnc -vnc_multiproc 8 -vnc_multicore 8
Run time
  reduce ~73% run-time with VNC default setting
 | ETM information |  |  | VNC flow | Local
cpu_top | post pglib | 5 modes | 31 corners | 1(H)16(M)28(S) | 4(H)24(M)18(S)
fzotg267nshn0u | pre lib pre pglib post lib post pglib | 3 modes | 20 corners 20 corners 62 corners 62 corners | 0(H)31(M)37(S) | 1(H)56(M)42(S)
VNC default setting
  VNC_PT_OS7
  4
  4

## Slide 19: Example - 1
Input
Command
  /home/eda/FTC_CADTOOL/EXE/merge_model.tcl -top fzotg267nshn0u -runpt -gendb
Output

## Slide 20: Example - 2
Input
Command
  /home/eda/FTC_CADTOOL/EXE/merge_model.tcl -top otn_top -runpt -gendb
Output

## Slide 21: Example - 3
Input
Command
  /home/eda/FTC_CADTOOL/EXE/merge_model.tcl -top fzotg267nshn0u -runpt -gendb
Output

## Slide 22: Merging Model Issue
Library file is invalid for merging
  Primetime returned
Solution
  Check if the input libraries are merged ETM. The merged ETM can not be merged again.
  How to check if the ETM is a merged ETM?
    grep if there is a keyword of “mode_definition” in ETM
% grep "mode_definition" otn_top_post_ffg0p99v125c_cmin.lib
# Returned nothing means this is not a merged ETM
% grep "mode_definition" merged_post_lib/otn_top_post_ffg0p99v125c_cmin.lib
mode_definition ( etm_modes_1 ) {
# If there is a “mode_definition” in ETM means this is a merged ETM

## Slide 23: Merging Model Issue
Found Different values defined for attribute (MODEL-18)
  Area
  Cell Leakage Power
Found inconsistent content (MODEL-20), (MODEL-23)
  Related PG pin
  Voltage Map
  Generated Clock
  Capacitance
Solution for issue 2 & 3:
  Re-gen ETM
Refer to Appendix 1.* for more detailed information of merging model issue

## Slide 24: Summary
single mode ETM + merge_model = merged ETM
library(“IP_capture”) {
...
pin(“...”) {
timing() {
** capture timing **
}
}
...
}
library(“IP_shift”) {
...
pin(“...”) {
timing() {
** shift timing **
}
}
...
}
library(“IP_merged”) {
...
mode_definition (etm_mode) {
mode_value (capture) {}
mode_value (shift) {}
}
...
pin(“...”) {
timing() {
mode (etm_mode, “capture”);
** capture timing **
}
timing() {
mode (etm_mode, “shift”);
** shift timing **
}
}
}
merge_model

## Slide 25: Summary
library(“IP_merged”) {
...
mode_definition (etm_mode) {
mode_value (capture) {}
mode_value (shift) {}
}
...
pin(“...”) {
timing() {
mode (etm_mode, “capture”);
** capture timing **
}
timing() {
mode (etm_mode, “shift”);
** shift timing **
}
}
}
library(“IP_merged”) {
...
pin(“...”) {
timing() {
mode (etm_mode, “capture”);
** capture timing **
}
timing() {
mode (etm_mode, “shift”);
** shift timing **
}
}
}
DISABLED
library(“IP_merged”) {
...
pin(“...”) {
timing() {
mode (etm_mode, “capture”);
** capture timing **
}
timing() {
mode (etm_mode, “shift”);
** shift timing **
}
}
}
DISABLED
set_mode shift
set_mode capture
merged ETM + set_mode = single mode ETM

## Slide 26: Reference
https://spdocs.synopsys.com/dow_retrieve/qsc-t/dg/ptolh/T-2022.03/ptolh/Content/ptug/ptug/hierarchical_analysis/etm/options/merging_extracted_models.htm
U:\DesignKitUsage\fetm\Merging_Extracted_Models.pdf
Testcase and QA result provided by IPT/Ann

## Slide 27: QA

## Slide 28: Thanks

## Slide 29: Appendix - 1.1
How to validate a merged ETM?
  We can validate a merged ETM by comparing the interface timing difference between single mode ETM and merged ETM.
How to build single mode ETM wrapper and merged ETM wrapper?
  PrimeTime generates a test design containing an instance of the extracted timing model as well as the extracted model itself.
What related files are required for merged ETM validation?
  single mode ETM, mode.sdc, mod_test.db, fetm working directory of single mode ETM
How to review the validation report?
  Check the interface timing difference
  Since there is no merged table in merged ETM, the interface timing difference should be zero

## Slide 30: Appendix - 1.2
flow chart
mode.sdc
mode_ETM
pt_shell
write_interface_timing
mode.tim
mode.sdc
set_mode …
merged_ETM
pt_shell
write_interface_timing
merged.tim
pt_shell
compare_interface_timing
merged_ETM_validation.rpt
Input files
  mode.sdc
  mode_ETM
  merged_ETM
  test.db
Output files
  mode.tim
  merged_ETM.tim
  merged_ETM_validation.rpt

## Slide 31: Appendix - 1.3
All of the input can be found in fetm working dir
Input
  mode SDC
    ${fetm_dir}/${TOP}_${mode}.sdc
    /home/FSJ0AS085A_PR/FSJ0AS085A/PartitionPR/lds_cpu/ETM/post/capture/lds_cpu_capture.sdc
  test.db
    ${fetm_dir}/${tmp_dir}/ETM/${TOP}_${mode}_${PVT}_${RC}/mod_test.db
    /home/FSJ0AS085A_PR/FSJ0AS085A/PartitionPR/lds_cpu/ETM/post/capture/tmpcapture_post/ETM/lds_cpu_capture_post_tt0p9v25c_typ/mod_test.db
    User should link the ${fetm_dir}/${tmp_dir}/ETM dir to the merging model dir

## Slide 32: Appendix - 1.4
Output
  model_validation/${TOP}_${mode}_${stage}_${PVT}_${RC}.rpt
  /home/dmd_proj/ollie_tsai_designkits_development/script/merge_model/val/model_validation/lds_cpu_capture_post_ffg0p99v125c_cmin.rpt
Report
  Since there is no merged table in merged ETM, the interface timing difference should be zero and status should be PASS

## Slide 33: Appendix - 1.5
Steps
  link all the single mode ETM to merging model dir
  link all the mode SDC to merging model dir
  mkdir ETM
  link all the ${fetm_dir}/${tmp_dir}/ETM/* to ETM/.
  merge_model.tcl -top ${TOP} -runpt -val
  The validating report will be in model_validation dir
inputs
outputs

## Slide 34: Appendix - 2.1
Inconsistent Related PG pin
  Primetime returned
  related_power_pin of ‘X_RREF’ in single mode ETM
  Solution
    Ask AC & RD check the PGPIN in PGMAP and re-gen ETM
Error: Found pin 'X_RREF' in the models defined with different related PG pin, cannot merge them. (MODEL-20)

## Slide 35: Appendix - 2.2
Inconsistent Voltage Map
  Primetime returned
  voltage_map of ‘VCC10R’ in single mode ETM
  Solution
    Ask AC & RD check the voltage in powervalue.list and re-gen ETM
Error: Found PG pin 'VCC10R' in the models defined with different voltage value, cannot merge them. (MODEL-20)
$ zgrep "voltage_map ( VCC10R" FXCMM0016HJ0P*_post_ffg0p99v0c_cmin.pglib.gz
FXCMM0016HJ0P_capture_post_ffg0p99v0c_cmin.pglib.gz: voltage_map ( VCC10R, 1.050000 );
FXCMM0016HJ0P_shift_post_ffg0p99v0c_cmin.pglib.gz: voltage_map ( VCC10R, 1.050000 );
FXCMM0016HJ0P_post_ffg0p99v0c_cmin.pglib.gz: voltage_map ( VCC10R, 1.100000 );

## Slide 36: Appendix - 2.3
Inconsistent Area
  Primetime returned
  Area in single mode ETM
  capture func
  Solution
    Ask AC & RD re-gen ETM with same setting (PT version) and design content (netlist, lib)
    Area is calculated by Primetime, and can be reviewed by command:
    get_attriburte [get_design $DESIGN]
Error: Found different values defined for attribute 'area', 478500.000000 and 461301.500000 in the models, cannot merge them. (MODEL-18)

## Slide 37: Appendix - 2.4
Inconsistent Capacitance
  Primetime returned
  Capacitance in single mode ETM
  Solution
    Ask AC & RD re-gen ETM
    Capacitance is calculated by Primetime
Error: Cannot merge pin 'TEST_CLK1' with different 'capacitance' 0.021336 and 0.023484 in the models. (MODEL-23)

## Slide 38: Appendix - 2.5
Inconsistent Cell Leakage Power
  Primetime returned
  single mode ETM
  Solution
    Ask AC & RD re-gen ETM
    The lib attribute, cell_leakage_power, is added by fetm according to powerdownfile
Error: Found different values defined for attribute 'cell_leakage_power', 1910537344.000000 and 8139100.000000 in the models, cannot merge them. (MODEL-18)

## Slide 39: Appendix - 2.6
Library file is invalid for merging
  Primetime returned
  Solution
    Check if the input libraries are merged ETM. The merged ETM can not be merged again.
    How to check if the ETM is a merged ETM?
      grep if there is a keyword of “MODE DEFINITION” in ETM
% grep "MODE DEFINITION" otn_top_post_ffg0p99v125c_cmin.lib
# Returned nothing means this is not a merged ETM
% grep "MODE DEFINITION“ merged_post_lib/otn_top_post_ffg0p99v125c_cmin.lib
/* MODE DEFINITIONS start here */
/* MODE DEFINITIONS end here */
# If there is a “MODE DEFINITION” in ETM means this is a merged ETM

## Slide 40: Appendix - 2.7
Inconsistent definition of generated clock
  Primetime returned
  Solution
    Ask AC & RD checks the clock definition in mode SDC and re-gen ETM

## Slide 41: Appendix 3.1
Updated on 2023/09/01
There is a new argument, “-tolerance 0”, in merging*.pt
  There is be a 0.04 tolerance by default, which brings merged values
  In this update, the tolerance is set to be 0, there will be no merged values
  If there are same values between multiple modes, there will be a merged table
timing () {
min_delay_flag : true ;
timing_type : min_clock_tree_path ;
timing_sense : positive_unate ;
mode(etm_modes_1, "capture shift");
/* comment : from another design; */
cell_rise( f_itrans ){
index_1 ( "0.000000, 0.004385, 0.015721, 0.037370, 0.071099, 0.150000, 0.469074");
values ( "0.070790, 0.072780, 0.076824, 0.081551, 0.086487, 0.093953, 0.111418");
}
cell_fall( f_itrans ){
index_1 ( "0.000000, 0.004385, 0.015721, 0.037370, 0.071099, 0.150000, 0.469074");
values ( "0.074075, 0.075893, 0.079613, 0.083946, 0.088340, 0.094877, 0.107735");
}
} /* end of arc sdh_sys_clk_sdh_sys_clk_mlat_min_2842*/

## Slide 42: Appendix 4.1
Current Faraday IP check-out rule
Note
  For 55nm or below, there will be only pglib in both “RD check-in IP flow lib” and “project-based check-out IP lib flow”
  For those users who want to have 55nm or below IP lib, they could try:
    Ask IPT to check-out IP package of older version
    Ask IP RD to share a local IP database
 | 55nm and below | others
lib content | merged ETM | merged ETM
lib type | .pglib | .lib / .pglib

## Slide 43: Enhancement History
2023/08/10 Fix the incorrect merged ETM file name issue
2023/08/11 Remove the ERROR msg which checks if there is only one ETM in the directory
2023/08/14 Add new option "-gendb" for generating merged.db automatically
2023/09/01 Add new argument "-tolerance 0" to merging*.pt, there will be no merged value in merged ETM (but still merged table if the values of modes are totally the same)
2023/09/19 Add checking PT and VNC setting steps
2023/09/19 enhance for VNC flow
2023/10/04 add option: -vnc_group, -vnc_multiproc, -vnc_multicore
2023/10/04 filter primetime WARNING message in merge_model.log
2023/10/11 enhance pvt_rc parser, ffgnp/ssgnp can be recognized correctly now
2023/10/20 enhance lsf flow
2023/10/27 new proc pplib and checkETMAttribute for post-processing missing is_pad into merged.pglib
2023/11/03 missing output_signal_level will be post-processed into merged.pglib and merged.lib
2023/11/27 new proc sanity_check, script checks single_mode/merged ETM by LC::check_library
2023/12/01 missing input_signal_level will be post-processed into merged.lib

## Slide 44
Confidential information
  The material is being disclosed to you pursuant to a non-disclosure agreement between you or your employer and Faraday. Information disclosed in this presentation may be used only as permitted under such an agreement.
Legal notice
  The information contained in this presentation is intended to provide a general guide as to which product is suited for a given requirement and shows suggested product applications. Specified functions and properties for products are only valid when handling instructions and other stated conditions and recommendations have been considered and followed. All descriptions, illustrations and dimensions in the information represent general particulars and do not form part of any contract. All information is provided “as is”, with no guarantee of completeness, accuracy, timeliness or of the results obtained from the use of the information, and without warranty of any kind, express or implied, including but not limited to warranties of performance. All information is subject to change without prior notice. Faraday assumes no responsibility whatsoever for any errors or inaccuracies about the information.

## Slide 45: Merged ETM Example
merge_models command
mode_definition in merged ETM